John Deere 1590

TO USERS OF THE NEW CASTLE CONSERVATION DISTRICT NO-TILL DRILL

Requires 85 HP with hydraulics, 3.5 tons, plants 10' with 7 inch rows

Can be pulled behind a heavy pickup (no half-tons), hitch must be extended beyond bumper to prevent damaging bumper.  Supply your own hitchpin. Calibration of the drill according to the "Operators Manual" found in the toolbox gives the best available estimate for the specific seeding rates.   The New Castle Conservation District accepts no responsibility for the accuracy of the setting.

NO FERTILIZER IS TO BE PUT IN SEED HOPPERS

LUBRICATE THE DRILL ACCORDING TO OPERATORS MANUAL Pg. 45 1-7

Before using the drill:

(	Check for any loose or broken parts.  Check Tires.

(	Check Seed Tubes for spider webs (especially small seed tubes).

(	Disengage the opener lock up valve and raise the hitch stand.

(	Install the safety chain.

(	Set the acreage meter to "O".

(	Operate at a ground speed of 4-6 mph.

(	Check lubrication.

Engage drive wheel.

After using the drill:

Disengage drive wheel.

(	Lock up the openers.

(	Clean out seed from all hoppers and tubes.  Vacuum or blow out the hoppers, clean out feed cups by dropping latch all the way down, and shake out the tubes.  If you used the small seed hopper, remove the drive chain and place in tool box.  There is a $50 hourly charge for not cleaning seed out of the drill.

(	Read the acreage meter.

Check lubrication.

(	Call Elizabeth Hook at 832-3100 extension 8970 to report completion and acres. The Drill will need to be returned to the District by renter unless there is another renter on the schedule. Call the District regarding return instructions.  The District will send you a bill.

Repairs Needed:

(	Call Elizabeth Hook at 832-3100 extension 8970.

(	If she is not available and parts or repairs are needed call Atlantic Tractor at 410-275-2195 in Cecilton, MD.